| Colour | Product Code | Pack Size | Box Qty |
| --- | --- | --- | --- |
| - | PATWIZ005 | 50ml | 24 |
|  | PATWIZ1 | 1Ltr | 12 |
|  | PATWIZ5 | 5Ltr | 4 |

Product Description

EVERBUILD PATIO WIZARD is a new type of Mould and Algae treatment that kills and cleans all type of green growth without the need for any washing off, scrubbing or pressure washing. Totally safe and non-hazardous to children and pets, once dry PATIO WIZARD is made from biodegradable ingredients and does not include any bleach or acid contents.

Available in either 5ltr and 1ltr concentrate or a 50ml super concentrate dissolving sachets in single clamp packs.

PATIO WIZARD is ideal for removing green growth from surfaces prior to painting, staining, sealing or applying roof coatings.

Benefits

- Fast acting.

- No need for washing or scrubbing after application.

- Powerful fast acting formula.

- HSE 9780 (super concentrate) HSE 9625 (concentrate) allowing sale in UK

- PCS Number 97716 (super concentrate) 97715 (concentrate) allowing sale in Ireland

Areas For Use

- Paved areas such as patios and driveways.

- Block Paving, fencing, sheds and greenhouses.

- Perspex, polycarbonate panels and garden furniture.

Limitations

- Dilute only as directed.

- Do not apply if rain is imminent (within 6 hours)

- For use only as specified as a surface biocide.

- On heavily soiled areas 2 applications may be required.

Application

50ml SACHET - Remove sachet from protective wrapper and simply drop into a bucket containing 5 Litres of water, ideally warm water to speed up dissolution which will take approx. 30-60 seconds, in cold water this may take up to 2-3 minutes, mix briefly before applying.

1 and 5ltr CONCNTRATE - Dilute with water at a maximum rate of 1 Part PATIO WIZARD to 9 Parts water, mix briefly before applying. Apply by watering can with a rose sprayer, garden sprayer, paint brush or sweeping brush depending upon area to be treated.

Whilst this product is designed to be safe to use on most ‘water safe’ surfaces we recommend that you test a small inconspicuous area if unsure.

Apply at an approximate rate of 1 litre per 3 to 6m². N.B: ensure any debris such as leaves, twigs, loose soil or weeds are removed from surfaces to be treated prior to application. After applying simply leave for 1 to 3 days and the green growth will slowly disappear (in a similar manner to the way weed killers work).

On heavily soiled surfaces a second application may be required.

5ltr concentrate pack will cover approx. 300 square metres depending on level of soiling. 50ml sachet will cover approx. 30 square metres.

Health & Safety

Consult MSDS for full list of hazards.

Storage

Protect from frost. Store only in original containers.

Shelf Life

This product should be used within 2 years of manufacture.

The technical data contained herein is based on our present knowledge and experience and we cannot be held liable for any errors, inaccuracies, omissions or editorial failings that result from technological changes or research between the date of issue of this document and the date the product is acquired. Before using the product, the user should carry out any necessary tests in order to ensure that the product is suitable for the intended application. Moreover, all users should contact the seller or the manufacturer of the product for additional technical information concerning its use if they think that the information in their possession needs to be clarified in any way, whether for normal use or a specific application of our product. Our guarantee applies within the context of the statutory regulations and provisions in force, current professional standards and in accordance with the stipulations set out in our general sales conditions. The information detailed in the present technical data sheet is given by way of indication and is not exhaustive. The same applies to any information provided verbally by telephone to any prospective or existing customer.

# Text boxes

EVERBUILD PATIO WIZARD